## Slide 1
Person Tracking Control of Mobile Robots Using a Lightweight Object Detection and Tracking System
I. Abstract
This paper aims to develop a lightweight person tracking control system to facilitate real-time pedestrian tracking tasks for mobile robots. The proposed system utilizes deep learning technology and lightweight network architecture to perform pedestrian detection tasks to achieve powerful pedestrian detection capabilities. Subsequently, the integration of multi-object tracking technology enables the system to effectively track identified pedestrian targets, thereby enabling real-time pedestrian tracking of mobile robots. Experimental results show that the proposed lightweight person tracking control system exhibits robust pedestrian following performance, stability, and effectiveness under various scenarios and environmental conditions. These properties increase the potential of the proposed system in many practical applications.
Keywords—Multi-object tracking, pedestrian detection, deep learning, person tracking control mobile robots.
    1. Feature Extraction: - The RGB image captured by the camera is input into the Feature Extraction Network. - This network extracts features of pedestrians from the image. 2. Object Detection: - The processed image is used for object detection through a lightweight detector. - OpenVINO is utilized for acceleration to enhance detection efficiency. 3. Track ID Decision: - A Track ID Decision module is designed to focus on a specific tracking target. - This module allows selection of a specific target ID to ensure focused tracking. 4. Following Control: - After locking onto the target ID, the system uses a P-Controller module to keep the target centered in the image. - The system outputs linear and angular velocity commands to control the mobile robot for target following actions.
II. THE PROPOSED PERSON TRACKING CONTROL SYSTEM
Figure 1 Block diagram of the proposed lightweight object detection and tracking system for visual tracking control of wheeled mobile robots
Figure 2 The EAIBOT SMART mobile robot used in this study. An RGBD camera is installed on the platform for person detection and tracking
Figure 4 Robustness of the proposed method to non-uniform ambient light conditions.
    Observation from Figure 3:
    - Multiple pedestrians are present, each with a unique ID.
    - The mobile robot successfully follows the target person with ID 1.
    - The system tracks only the target with ID 1, ensuring focus even in multi-person scenarios.
    - The output linear velocity maintains the desired level.
    - The output angular velocity correctly responds to the target‘s movement.
    Experimental Results from Figure 4:
    - The tracking control system is robust to ambient light changes.
    - The mobile robot stably follows the target even under non-uniform background light.
    - Accurate tracking is maintained under very low lighting conditions.
    - The results validate the performance and robustness of the tracking control system.
Figure 3 Corresponding linear and angular velocity commands of the mobile robot.
The proposed tracking control system can continuously lock the specific person with ID 1 and continue tracking in a multi-pedestrian environment.
In this paper, we developed a real-time lightweight target detection and tracking system based on deep learning and Multi-Object Tracking (MOT) System. The advantage of using MOT technology is that it allows simultaneous tracking of multiple individuals in a scene, distinguishing the tracked target person from other pedestrians. Additionally, this system employs a lightweight detector to meet real-time computational requirements and exhibits robust tracking performance under non-uniform ambient lighting conditions. Experimental results demonstrate that the tracking control performance of this system is quite robust, making it suitable for personnel tracking control applications in mobile robots. This provides valuable insights for the development of mobile robot tracking control systems.
IV. CONCLUSION
Robotics and Automation Sciences
Paper Title
Supervisor
PhD Candidate
Yu-Chen Chiu
Master Student
Huan-Wei Hsu
:
:
Chi-Yi Tsai
Paper ID
S304
:
III. EXPERIMENTAL RESULTS